## Slide 1: Feature Detection
Instructor
LE Thanh Sach, Ph.D.
Ltsach@cse.hcmut.edu.vn
http://www.cse.hcmut.edu.vn/~ltsach/

## Slide 2: Outline
Image features
Corner feature:
  Moravec
  Harris
Scale Invariant Feature Transform (SIFT)
Speed Up Robust Features (SURF)
Gradient Location Orientation Histogram (GLOH)
Multi-Scale Oriented Patches (MSOP)
Feature Matching

## Slide 3: Feature: Concept
Feature can be defined as the information which is extracted (detect + describe) from images and is aimed to be used for further tasks in computer vision, for examples, classification, matching, and tracking.
?
Notes: 3

## Slide 4: Feature: Assessment Criteria
Distinctive: a single feature can be correctly matched with high probability.
Invariant: invariant to scale, rotation, affine, illumination and noise for robust matching across a substantial range of affine distortion, viewpoint change and so on.
Notes: 4

## Slide 5: Feature: Tasks
Feature detection locates where they are
Feature description describes what they are
Feature matching decides whether two are the same one
Notes: 5

## Slide 6: Corner detector
Notes: 6

## Slide 7: Moravec corner detector (1980)
Corner point:
  Be easily recognized by looking through a small window
  Shift a window in any direction should give a large change in intensity
Notes: 7

## Slide 8: Moravec corner detector
flat
Notes: 8

## Slide 9: Moravec corner detector
flat
Notes: 9

## Slide 10: Moravec corner detector
flat
edge
Notes: 10

## Slide 11: Moravec corner detector
flat
edge
corner
isolated point
Notes: 11

## Slide 12: Moravec corner detector
Change of intensity for the shift [u,v]:
window function
intensity
shifted intensity
Notes: 12

## Slide 13: Moravec corner detector
Change of intensity for the shift [u,v]:
window function
intensity
shifted intensity
Four shifts: (u,v) = (1,0), (1,1), (0,1), (-1, 1)
Look for local maxima in  min{E(u,v)}
Notes: 13

## Slide 14: Problems of Moravec detector
(Problem 1): Noisy response
  due to a binary window function
(Problem 2): Only a set of shifts at every 45 degree is considered
(Problem 3): Only minimum of E is taken into account
Harris corner detector (1988) solves these problems.
Notes: 14

## Slide 15: Harris corner detector
(Problem 1): Noisy response due to a binary window function
Use a Gaussian function
Notes: 15

## Slide 16: Harris corner detector
(Problem 2): Only a set of shifts at every 45 degree is considered
 Consider all small shifts by Taylor’s expansion
Notes: 16

## Slide 17: Harris corner detector
Taylor expansion:
(1st order)
(2nd order)
(3rd order)
(higher order)
Notes: 17

## Slide 18: Harris corner detector
1st order approximation:
Notes: 18

## Slide 19: Harris corner detector
(1st approximation)
(matrix form)
Notes: 19

## Slide 20: Harris corner detector
Equivalently, for small shifts [u,v] we have a bilinear approximation:
Where M is a 22 matrix computed from image derivatives:
Notes: 20

## Slide 21: Harris corner detector (matrix form)
Notes: 21

## Slide 22: Harris corner detector
Only minimum of E is taken into account
A new corner measurement by investigating the shape of the error function
represents a quadratic function; Thus, we can analyze E’s shape by looking at the property of M
Notes: 22

## Slide 23: Harris corner detector
High-level idea: what shape of the error function will we prefer for features?
flat
edge
corner

## Slide 24: Quadratic forms
Quadratic form (homogeneous polynomial of degree two) of n variables xi
Examples
=
Notes: 24
See W W L Chen’s linear algebra book, chap 11

## Slide 25: Symmetric matrices
Quadratic forms can be represented by a real symmetric matrix A where
Notes: 25

## Slide 26: Symmetric matrices
Quadratic forms can be represented by a real symmetric matrix A where
Notes: 26

## Slide 27: Eigenvalues of symmetric matrices
Brad Osgood
Notes: 27

## Slide 28: Eigenvectors of symmetric matrices
Notes: 28

## Slide 29: Eigenvectors of symmetric matrices
Notes: 29
藍色座標系內的正圓在黑色座標系內看起來變成橢圓。

## Slide 30: Harris corner detector
Intensity change in shifting window: eigenvalue analysis
1, 2 – eigenvalues of M
direction of the slowest change
direction of the fastest change
(max)-1/2
(min)-1/2
Ellipse E(u,v) = const
Notes: 30

## Slide 31: Visualize quadratic functions
Notes: 31

## Slide 32: Visualize quadratic functions
Notes: 32

## Slide 33: Visualize quadratic functions
Notes: 33

## Slide 34: Visualize quadratic functions
Notes: 34

## Slide 35: Harris corner detector
1
2
Corner
1 and 2 are large, 1 ~ 2; E increases in all directions
1 and 2 are small; E is almost constant in all directions
edge 1 >> 2
edge 2 >> 1
flat
Classification of image points using eigenvalues of M:
Notes: 35

## Slide 36: Harris corner detector
Measure of corner response:
(k – empirical constant, k = 0.04-0.06)
Only for reference,
you do not need
them to compute R
Notes: 36
http://mathworld.wolfram.com/Eigenvalue.html

## Slide 37: Harris corner detector
Notes: 37

## Slide 38: Another view
Notes: 38

## Slide 39: Another view
Notes: 39

## Slide 40: Another view
Notes: 40

## Slide 41: Summary of Harris detector
Compute x and y derivatives of image
Compute products of derivatives at every pixel
Compute the sums of the products of derivatives at each pixel

## Slide 42: Summary of Harris detector
Define the matrix at each pixel
Compute the response of the detector at each pixel
Threshold on value of R; compute nonmax suppression.

## Slide 43: Harris corner detector (input)
Notes: 43

## Slide 44: Corner response R
Notes: 44

## Slide 45: Threshold on R
Notes: 45

## Slide 46: Local maximum of R
Notes: 46

## Slide 47: Harris corner detector
Notes: 47

## Slide 48: Harris detector: summary
Average intensity change in direction [u,v] can be expressed as a bilinear form:
Describe a point in terms of eigenvalues of M: measure of corner response
A good (corner) point should have a large intensity change in all directions, i.e. R should be large positive
Notes: 48

## Slide 49: Now we know where features are
But, how to match them?
What is the descriptor for a feature? The simplest solution is the intensities of its spatial neighbors. This might not be robust to brightness change or small shift/rotation.
(
)
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9
Notes: 49

## Slide 50: Harris detector: some properties
Partial invariance to affine intensity change
Only derivatives are used => invariance to intensity shift I  I + b
Intensity scale: I  a I
R
x (image coordinate)
threshold
R
x (image coordinate)
Notes: 50

## Slide 51: Harris Detector: Some Properties
Rotation invariance
Ellipse rotates but its shape (i.e. eigenvalues) remains the same
Corner response R is invariant to image rotation
Notes: 51

## Slide 52: Harris Detector is rotation invariant
Repeatability rate:
# correspondences # possible correspondences
Notes: 52

## Slide 53: Harris Detector: Some Properties
But: not invariant to image scale!
All points will be classified as edges
Corner !
Notes: 53

## Slide 54: Harris detector: some properties
Quality of Harris detector for different scale changes
Repeatability rate:
# correspondences # possible correspondences
Notes: 54

## Slide 55: Scale invariant detection
Consider regions (e.g. circles) of different sizes around a point
Regions of corresponding sizes will look the same in both images
Notes: 55

## Slide 56: Scale invariant detection
The problem: how do we choose corresponding circles independently in each image?
Aperture problem
Notes: 56

## Slide 57: SIFT (Scale Invariant Feature Transform)
Notes: 57

## Slide 58: SIFT
SIFT is an carefully designed procedure with empirically determined parameters for the invariant and distinctive features.
Notes: 58

## Slide 59: SIFT stages:
Scale-space extrema detection
Keypoint localization
Orientation assignment
Keypoint descriptor
( )
local descriptor
detector
descriptor
A 500x500 image gives about 2000 features
Notes: 59

## Slide 60: 1. Detection of scale-space extrema
For scale invariance, search for stable features across all possible scales using a continuous function of scale, scale space.
SIFT uses DoG filter for scale space because it is efficient and as stable as scale-normalized Laplacian of Gaussian.
Notes: 60

## Slide 61: 1. Detection of scale-space extrema DoG filtering
Convolution with a variable-scale Gaussian
Difference-of-Gaussian (DoG) filter
Convolution with the DoG filter
Notes: 61

## Slide 62: 1. Detection of scale-space extrema Scale space

k
2
2k
2k2

k
2
2k
Notes: 62

## Slide 63: 1. Detection of scale-space extrema Scale space
D(x,y, 0)
D(x,y, 1)
D(x,y, 2)
D(x,y, 3)
Notes: 63

## Slide 64: 1. Detection of scale-space extrema Examples
Notes: 64

## Slide 65: 1. Detection of scale-space extrema Key-points localization
X is selected as a key-point,
if it is larger or smaller than all 26 neighbors
Point: X
Coordinate: D(x,y,)
Notes: 65

## Slide 66: 1. Detection of scale-space extrema Decide scale sampling frequency
It is impossible to sample the whole space, tradeoff efficiency with completeness.
Decide the best sampling frequency by experimenting on 32 real image subject to synthetic transformations. (rotation, scaling, affine stretch, brightness and contrast change, adding noise…)
Notes: 66

## Slide 67: 1. Detection of scale-space extrema Decide scale sampling frequency
Notes: 67

## Slide 68: 1. Detection of scale-space extrema Decide scale sampling frequency
s=3 is the best, for larger s, too many unstable features
for detector,
repeatability
for descriptor,
distinctiveness
Notes: 68

## Slide 69: 1. Detection of scale-space extrema Pre-smoothing
 =1.6, plus a double expansion
Notes: 69

## Slide 70: 1. Detection of scale-space extrema Scale Invariance
Notes: 70

## Slide 71: 2. Accurate key-point localization
Fit a 3D quadratic function for finding sub-pixel maxima
Reject key-points with low contrast areas
Reject key-points on edges
Notes: 71

## Slide 72: 2. Accurate keypoint localization: Fit a 3D quadratic function
Idea:
1
6
5
0
-1
+1
Find them
Notes: 72

## Slide 73: 2. Accurate keypoint localization: Fit a 3D quadratic function
Idea:
1
6
5
0
-1
+1
Notes: 73

## Slide 74: 2. Accurate keypoint localization: Fit a 3D quadratic function
Idea:
  Use Taylor Expansion:
If Minimum/Maximum is at then
is the solution of the following equation:
Minimum/Maximum is:
Notes: 74

## Slide 75: 2. Accurate key-point localization: Fit a 3D quadratic function
1
6
5
0
-1
+1
Notes: 75

## Slide 76: 2. Accurate key-point localization: Fit a 3D quadratic function
Where,
Notes: 76

## Slide 77: 2. Accurate key-point localization: Fit a 3D quadratic function
Scalar
Vector: 1×3
Matrix: 3×3
Notes: 77

## Slide 78: 2. Accurate key-point localization: Fit a 3D quadratic function
How to compute derivatives, for example, 2D function f(x,y):
f(x,y)
Derivatives:
Notes: 78

## Slide 79: 2. Accurate key-point localization: Fit a 3D quadratic function
Derivatives:
Notes: 79

## Slide 80: 2. Accurate key-point localization: Fit a 3D quadratic function
Derivatives:
Notes: 80

## Slide 81: 2. Accurate key-point localization: Fit a 3D quadratic function
Derivatives:
Notes: 81

## Slide 82: 2. Accurate key-point localization: Fit a 3D quadratic function
Finding maximum/minimum by solving the following equation:
Notes: 82

## Slide 83: 2. Accurate key-point localization: Fit a 3D quadratic function
Question:
How to compute derivative of the following forms?
Notes: 83

## Slide 84: 2. Accurate key-point localization: Fit a 3D quadratic function
Notes: 84

## Slide 85: 2. Accurate key-point localization: Fit a 3D quadratic function
Notes: 85

## Slide 86: 2. Accurate key-point localization: Fit a 3D quadratic function
Notes: 86

## Slide 87: 2. Accurate key-point localization: Fit a 3D quadratic function
Differentiate two sides
(A is symmetric)
Notes: 87

## Slide 88: 2. Accurate key-point localization: Fit a 3D quadratic function
Maximum/Minimum is the solution of:
Notes: 88

## Slide 89: 2. Accurate key-point localization: Fit a 3D quadratic function
Maximum/Minimum at:
Maximum/Minimum is:
Notes: 89

## Slide 90: 2. Accurate key-point localization: Reject key-points at low contrast areas
If any dimension of is larger than 0.5: change sample point
If : Throw out the minimum/maximum
Notes: 90

## Slide 91: 2. Accurate key-point localization: Reject key-points on edges
r=10
Let
Keep the points with
Hessian matrix at keypoint location
Notes: 91

## Slide 92: 2. Accurate key-point localization: Examples
Notes: 92

## Slide 93: 2. Accurate key-point localization: After removing points at low contrast areas or on edges
Notes: 93

## Slide 94: 2. Accurate key-point localization: Other examples
233x89
832 extrema
729 after con-
trast filtering
536 after cur-
vature filtering
Notes: 94

## Slide 95: 3. Orientation assignment
By assigning a consistent orientation, the keypoint descriptor can be orientation invariant.
For a keypoint, L is the Gaussian-smoothed image with the closest scale,
Notes: 95

## Slide 96: 3. Orientation assignment Compute orientation
orientation histogram (36 bins)
(Lx, Ly)
m
θ
Notes: 96

## Slide 97: 3. Orientation assignment Examples
Notes: 97

## Slide 98: 3. Orientation assignment Demonstration
Notes: 98

## Slide 99: 3. Orientation assignment Demonstration
Notes: 99

## Slide 100: 3. Orientation assignment Determine the most important orientation
σ = 1.5*scale of the key-point
a. Weighting the gradient’s magnitude of key-points, using Gaussian function.
Notes: 100

## Slide 101: 3. Orientation assignment Determine the most important orientation
b. Computing the histogram of the gradient’s magnitude of key-points.
Notes: 101

## Slide 102: 3. Orientation assignment Determine the most important orientation
c. Finding the histogram’s peaks. Using fitting to obtain accurate the peaks’ position
Notes: 102

## Slide 103: 3. Orientation assignment Determine the most important orientation
Notes: 103

## Slide 104: 3. Orientation assignment Determine the most important orientation
36-bin orientation histogram over 360°, weighted by m and 1.5*scale falloff
Peak is the orientation
Local peak within 80% creates multiple orientations
About 15% has multiple orientations and they contribute a lot to stability
Summarization
Notes: 104

## Slide 105: 3. Orientation assignment The most important orientation: Demo
Notes: 105

## Slide 106: 4. Local image descriptor
Most important orientation
A Key-point
Gradient sub-image
Size: 16×16 cells
Cell: pixel or resampled cell
Gaussian function for weighting magnitudes
 = 0.5 window’ size
Notes: 106

## Slide 107: 4. Local image descriptor
a. Divide key-point’s window into 4×4 cells
b. Create 8-bin histogram for gradients inside each cell
A feature vector has 4×4×8 = 128 components
Notes: 107

## Slide 108: 4. Local image descriptor Why 4x4x8?
Notes: 108

## Slide 109: 4. Local image descriptor Sensitivity to affine change
Notes: 109

## Slide 110: Feature matching
for a feature x, he found the closest feature x1 and the second closest feature x2. If the distance ratio of d(x, x2) and d(x, x1) is smaller than 0.8, then it is accepted as a match.
Notes: 110

## Slide 111: SIFT: Summary Create scale-space
Notes: 111

## Slide 112: SIFT: Summary Determine extrema
Notes: 112

## Slide 113: SIFT: Summary Remove low contrast points
Notes: 113

## Slide 114: SIFT: Summary (Vfeat) Remove edge points
Notes: 114

## Slide 115: SIFT: Summary Generate descriptor
Notes: 115

## Slide 116: SURF Speeded Up Robust Features

## Slide 117: SURF: Speeded Up Robust Features
Speed-up computations by fast approximation of (i) Hessian matrix and (ii) descriptor using “integral images”.
What is an “integral image”?
Herbert Bay, Tinne Tuytelaars, and Luc Van Gool, “SURF: Speeded Up Robust Features”, European Computer Vision Conference (ECCV), 2006.
Notes: 117
117

## Slide 118: Integral Image
The integral image IΣ(x,y) of an image I(x, y) represents the sum of all pixels in I(x,y) of a rectangular region formed by (0,0) and (x,y).
.
Using integral images, it takes only four array references to calculate the sum of pixels over a rectangular region of any size.
Notes: 118
118

## Slide 119: SURF: Speeded Up Robust Features (cont’d)
Approximate Lxx, Lyy, and Lxy using box filters
Those values can be computed very fast using integral images!
Notes: 119
119

## Slide 120: SURF: Speeded Up Robust Features (cont’d)
(box filters shown are 9 x 9
– good approximations for a Gaussian with σ=1.2)
derivative
approximation
approximation
derivative
Notes: 120
120

## Slide 121: SURF
In SIFT
  Original images are repeatedly smoothed with a Gaussian
  Then, sub-sampled to achieve a higher level of the pyramid.
Notes: 121
121

## Slide 122: SURF
In SURF:
  use filters of larger size on the original image.
  SPEED-UP: use integral images to compute the filter’s response
Notes: 122
122

## Slide 123: SURF vs. SIFT
Approximation of H:
Using DoG
Using box filters
Notes: 123
123

## Slide 124: SURF
Instead of using a different measure for selecting the location and scale of interest points (e.g., Hessian and DOG in SIFT), SURF uses the determinant of to find both.
Determinant elements must be weighted to obtain a good approximation:
Notes: 124
124

## Slide 125: SURF
Once interest points have been localized both in space and scale, the next steps are:
  (1) Orientation assignment
  (2) Keypoint descriptor
Notes: 125
125

## Slide 126: SURF
Orientation assignment
Circular neighborhood of
radius 6σ around the interest point
(σ = the scale at which the point was detected)
x response y response
Can be computed very fast using integral images!
600
window
dx
dy
Haar wavelets (responses weighted with Gaussian)
side length = 4σ
Notes: 126
126

## Slide 127
Orientation assignment
  - The image is convoluted with two first-order Haar wavelets.
  - The filter responses at certain sampling points around the keypoint are represented as a vector in a two-dimensional space.
  - A rotating window of 600 is used to sum up all vectors within its range, and the longest resulting vector determines the orientation.
SURF

## Slide 128: SURF
Sum the response over each sub-region for dx and dy separately.
To bring in information about the polarity of the intensity changes, extract the sum of absolute value of the responses too.
Feature vector size:
4 x 16 = 64
Keypoint descriptor (square region of size 20σ)
4 x 4
grid
Notes: 128
128

## Slide 129: SURF
SURF-128
  The sum of dx and |dx| are computed separately for points where dy < 0 and dy >0
  Similarly for the sum of dy and |dy|
  More discriminatory!
Notes: 129
129

## Slide 130: SURF: Speeded Up Robust Features
Has been reported to be 3 times faster than SIFT.
Less robust to illumination and viewpoint changes compared to SIFT.
K. Mikolajczyk and C. Schmid,"A Performance Evaluation of Local Descriptors",
IEEE Transactions on Pattern Analysis and Machine Intelligence, vol. 27, no. 10,
pp. 1615-1630, 2005.
Notes: 130
130

## Slide 131: SIFT extensions
Notes: 131

## Slide 132: PCA
Notes: 132

## Slide 133: PCA-SIFT
Only change step 4
Pre-compute an eigen-space for local gradient patches of size 41x41
2x39x39=3042 elements
Only keep 20 components
A more compact descriptor
Notes: 133

## Slide 134: GLOH (Gradient location-orientation histogram)
17 location bins
16 orientation bins
Analyze the 17x16=272-d
eigen-space, keep 128 components
SIFT is still considered the best.
SIFT
Notes: 134

## Slide 135: Multi-Scale Oriented Patches
Simpler than SIFT. Designed for image matching. [Brown, Szeliski, Winder, CVPR’2005]
Feature detector
  Multi-scale Harris corners
  Orientation from blurred gradient
  Geometrically invariant to rotation
Feature descriptor
  Bias/gain normalized sampling of local patch (8x8)
  Photometrically invariant to affine changes in intensity
Notes: 135

## Slide 136: Multi-Scale Harris corner detector
Image stitching is mostly concerned with matching images that have the same scale, so sub-octave pyramid might not be necessary.
Notes: 136

## Slide 137: Multi-Scale Harris corner detector
smoother version of gradients
Corner detection function:
Pick local maxima of 3x3 and larger than 10
Notes: 137

## Slide 138: Keypoint detection function
Experiments show roughly
the same performance.
Notes: 138

## Slide 139: Non-maximal suppression
Restrict the maximal number of interest points, but also want them spatially well distributed
Only retain maximums in a neighborhood of radius r.
Sort them by strength, decreasing r from infinity until the number of keypoints (500) is satisfied.
Notes: 139

## Slide 140: Non-maximal suppression
Notes: 140

## Slide 141: Sub-pixel refinement
Notes: 141

## Slide 142: Orientation assignment
Orientation = blurred gradient
Notes: 142

## Slide 143: Descriptor Vector
Rotation Invariant Frame
  Scale-space position (x, y, s) + orientation ()
Notes: 143

## Slide 144: MSOP descriptor vector
8x8 oriented patch sampled at 5 x scale. See TR for details.
Sampled from with spacing=5
8 pixels
40 pixels
Notes: 144

## Slide 145: MSOP descriptor vector
8x8 oriented patch sampled at 5 x scale. See TR for details.
Bias/gain normalisation: I’ = (I – )/
Wavelet transform
8 pixels
40 pixels
Notes: 145

## Slide 146: Detections at multiple scales
Notes: 146

## Slide 147: Summary
Multi-scale Harris corner detector
Sub-pixel refinement
Orientation assignment by gradients
Blurred intensity patch as descriptor
Notes: 147

## Slide 148: Feature matching
Exhaustive search
  for each feature in one image, look at all the other features in the other image(s)
Hashing
  compute a short descriptor from each feature vector, or hash longer descriptors (randomly)
Nearest neighbor techniques
  k-trees and their variants (Best Bin First)
Notes: 148

## Slide 149: Wavelet-based hashing
Compute a short (3-vector) descriptor from an 8x8 patch using a Haar “wavelet”
Quantize each value into 10 (overlapping) bins (103 total entries)
[Brown, Szeliski, Winder, CVPR’2005]
Notes: 149

## Slide 150: Nearest neighbor techniques
k-D tree and
Best Bin First (BBF)
Indexing Without Invariants in 3D Object Recognition, Beis and Lowe, PAMI’99
Notes: 150

## Slide 151: Applications
Notes: 151

## Slide 152: Recognition
SIFT Features
Notes: 152

## Slide 153: 3D object recognition
Notes: 153

## Slide 154: 3D object recognition
Notes: 154

## Slide 155: Office of the past
Video of desk
Images from PDF
Track & recognize
T
T+1
Internal representation
Scene Graph
Desk
Desk
Notes: 155

## Slide 156: Image retrieval
…
> 5000
images
change in viewing angle
Notes: 156

## Slide 157: Image retrieval
22 correct matches
Notes: 157

## Slide 158: Image retrieval
…
> 5000
images
change in viewing angle
+ scale change
Notes: 158

## Slide 159: Robot location
Notes: 159

## Slide 160: Robotics: Sony Aibo
SIFT is used for
Recognizing charging station
Communicating with visual cards
Teaching object recognition
soccer
Notes: 160

## Slide 161: Structure from Motion
The SFM Problem
  Reconstruct scene geometry and camera motion from two or more images
Track
2D Features
Estimate
3D
Optimize
(Bundle Adjust)
Fit Surfaces
SFM Pipeline
Notes: 161

## Slide 162: Structure from Motion
Poor mesh
Good mesh
Notes: 162

## Slide 163: Augmented reality
Notes: 163

## Slide 164: Automatic image stitching
Notes: 164

## Slide 165: Automatic image stitching
Notes: 165

## Slide 166: Automatic image stitching
Notes: 166

## Slide 167: Automatic image stitching
Notes: 167

## Slide 168: Automatic image stitching
Notes: 168

## Slide 169: Reference
Chris Harris, Mike Stephens, A Combined Corner and Edge Detector, 4th Alvey Vision Conference, 1988, pp147-151.
David G. Lowe, Distinctive Image Features from Scale-Invariant Keypoints, International Journal of Computer Vision, 60(2), 2004, pp91-110.
Yan Ke, Rahul Sukthankar, PCA-SIFT: A More Distinctive Representation for Local Image Descriptors, CVPR 2004.
Krystian Mikolajczyk, Cordelia Schmid, A performance evaluation of local descriptors, Submitted to PAMI, 2004.
SIFT Keypoint Detector, David Lowe.
Matlab SIFT Tutorial, University of Toronto.
Notes: 169